## Slide 1: Darcy’s Law - Introduction
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Darcy’s Experiments
Henry Darcy did some lab tests on flow through sand in order to design filters
*Published in “The Public Fountains of the City of Dijon” - 1856

## Slide 3: Darcy’s Law
Darcy experimented with different soils and with different values of L, h1, and h2. The results showed that:
where:
q = DVol/Dt = flow rate [L3/T]
k = coefficient of permeability
or hydraulic conductivity [L/T]
A = gross cross-sectional area of flow [L2]
h = total head [L]
L = length of flow path [L]

## Slide 4: Alternate Formulation
Darcy's law is often written as:
q = kiA
where s is the flow path length
i = hydraulic gradient
where:

## Slide 5: Darcian vs. Seepage Velocity
Darcy's law can be rewritten as:
q = kiA
vd = ki
vd = "discharge velocity" or "Darcian velocity"
Vs
Vd
vs = "seepage velocity"

## Slide 6: Seepage Velocity
Seepage velocity can be related to discharge velocity as follows:
Vv = Volume of soil voids
V = Total volume
n = porosity

## Slide 7: Seepage Velocity, cont.
n | vs/vd
0.25 | 4
0.3 | 3.33
0.35 | 2.9
0.4 | 2.5
n = porosity
total area
area
=

## Slide 8: Effective Porosity
Not all voids in the soil conduct flow.
ne = "effective" porosity
where Af = actual area of flow

## Slide 9: Effective Porosity, cont.
ne = ln
l = effective porosity factor
l is determined experimentally
l  1 for sands and gravels
l = 0.01 - 0.05 for clays or fractured rock

## Slide 10: Permeability
In the equation for Darcy's law:
q = kiA
k is a constant which depends on both the fluid and the soil.
where:
K = "constant of proportionality“ [L2]
or "intrinsic permeability"
or "permeability"
K is based on soil properties only
gf = unit weight of fluid [F/L3]
m = viscosity of fluid [ML/T]
Darcy's law can be rewritten as:

## Slide 11: Permeability, cont.
Can also be written as:
This form is used in the petroleum industry.
K is often expressed in units of Darcies
1 Darcy = the permeability for a flow of 1 cm3/sec/cm2 for a viscosity of 1 centipoise and [rg(dh/dx)] = 1 atm/cm.
1 poise = 1 dyne-sec/cm2 = 1 g/cm-s
1 Darcy = 0.987X10-8 cm2
For water at 20o C:
mw = 0.0100 poise
gw = rwg
rw = 1 g/cm3
g = 980.7 cm/sec2
for k = 1 cm/s: K = 1.02X10-5 cm2
We will use k (hydraulic conductivity) in this class.

## Slide 12: Typical Values of K
http://en.wikipedia.org/wiki/Hydraulic_conductivity