## Slide 1: Governing Differential Equations
CE EN 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Background
All of the flow conditions we have seen so far have been simple, 1-D problems where we could use Darcy’s Law directly. In most applications, however, the geometry and soil properties are more complex, and a more complete governing equation is needed.
The following derivation is a general form of the 3D case.

## Slide 3: Assumptions
Soil is saturated
  We could derive the equations to describe unsaturated flow, but we will stick to saturated flow in this class.
Darcy's law is valid
Mass is conserved
  i.e., what goes in must come out or be stored based on conservation of mass.

## Slide 4: Steady State Saturated Flow
inflow - outflow = 0
First, we will consider a special case where we have steady state conditions (system is in equilibrium - no change with time) and no sources/sinks. Thus, the two terms on right will be set to zero.

## Slide 5: Steady State Saturated Flow
inflow - outflow = 0
mass flow rate = r v

## Slide 7
(inflow - outflow)total = (inflow - outflow)x
+ (inflow - outflow)y
+ (inflow - outflow)z = 0

## Slide 8
Assume that the fluid density is constant:
Use Darcy's law to express velocity:

## Slide 9
Substituting vx, vy, and vz:

## Slide 10
Combining terms:
If x, y, and z correspond to principal axes of permeability:

## Slide 11
More commonly written as:
if kx = ky = kz:
The solution to any of these equations is a function describing h in terms of x, y, and z
"Laplace Equation"
h(x, y, z)

## Slide 12: Boundary Conditions
As with any differential equation, before we can solve for h(x, y, z), we must define some boundary conditions.
The following slides illustrate how boundary conditions are determined on some typical problems.

## Slide 17: Solution
For simple cases we can solve for an analytical solution.
For more general (complicated) cases, we use a graphical solution (flow net) or a numerical solution (finite difference or finite element).

## Slide 18: Sources and Sinks
Sources/sinks = wells, rivers, recharge, etc.
Changes mass balance of governing equation:
Where R =
Re-derivation leads to:

## Slide 19: Transient Flow
The amount of water in the representative element may change over time due to expansion and contraction of the porous media.
represents the change in mass stored in the system.

## Slide 20: Transient Flow
Following a similar strategy, we can derive the following governing equation:
where:
Ss = specific storage
We will review a full derivation of the transient terms later in the semester