## Slide 1: MODFLOW – Organization & Main Packages
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Code Selection – Model Design
We are now at this spot in the model development process
MODFLOW is generally a safe and dependable choice for a model code
Model design = construction of numerical grid and model inputs

## Slide 3
Developed by McDonald & Harbaugh of the USGS, 1983
Public Domain, open source
Most widely used groundwater model
Steady-state or transient saturated flow
Versions:
  MODFLOW 88
  MODFLOW 96
  MODFLOW 2000
  MODFLOW 2005
  MODFLOW-NWT
  MODFLOW-USG
  MODFLOW 6

## Slide 4: Finite Difference Model
3D Cartesian Grid Cell-Centered

## Slide 5: Grid Geometry
Orthogonal in xy
Thickness varies in z

## Slide 6: MODFLOW-USG
New version of MODFLOW that allows for unstructured grids (no rows/columns/layers). Uses finite volume formulation.
Allows for more efficient grid refinement around features where rapid head change occurs.

## Slide 7: Governing Equation
where:
Kxx, Kyy, Kzz = values of hyd. cond. along xyz axes
h = total head
W = Sources and sinks
Ss = Specific storage
t = time

## Slide 8: Processes & Packages
MODFLOW is divided into a series of processes & packages
Major tasks are organized as processes
More specific tasks are performed by packages
Each process may use one or more packages

## Slide 9: Global Process
Spatial discretization
  # rows, cols, layers
  Top/bottom elevations
Temporal discretization
  Stress periods
  Time steps
Units (ft vs m, etc)
Package Selection
Notes: There is a layer discretization file and a global package file that are used by the Global Process.

## Slide 10: Ground Water Flow Process
Formulation and solution of the ground water flow equation by the FD method
Main part of MODFLOW code
Includes
  Flow package (BCF, LPF, or HUF)
  Source/sink packages
  Solvers

## Slide 11: Observation Process
Used for model calibration
Calculates model-simulated heads and discharges to sources/sinks

## Slide 12: Required Packages
Discretization
  Rows, columns, layers (number and dimension)
Basic
  Active cells (IBOUND)
  Starting heads
Output Control
  What should be written to output files and at what frequency
Flow Package (BCF, *LPF, HUF, UPW)
  Aquifer properties (K, Ss, etc)
Solver (SIP, SSOR, *PCG, GMG, etc.)
*Default selection in GMS

## Slide 13: Active/Inactive Zones
Cells outside problem domain are marked as inactive
Controlled by IBOUND array
(1=active, 0=inactive, -1=specified head)

## Slide 14: Virginia Coastal Plain Model
Notes: http://va.water.usgs.gov/online_pubs/WRIR/98-4085/g-wfmcpasys_va.html

## Slide 15: Flow Packages
Defines aquifer properties
Four options
  Block-Centered Flow (BCF)
  Layer Property Flow (LPF)*
  Hydrogeologic Unit Flow (HUF)
  Upstream Weighting (UPW), MODFLOW-NWT
*We will use the LPF package in this course

## Slide 16: LPF - Layer Property Flow Package
User enters Kh, Kv and storage terms for all layers
Kv can be entered as directly or in terms of vertical anisotropy
Horizontal anisotropy entered on a cell-by-cell basis
Two layer types
  Confined
  Convertible

## Slide 17: Optional Packages
CHB – Time Variant Specified Head
DRN – Drain
DRT – Drain Return Flow
ETS – Evapotranspiration Segments
EVT – Evapotranspiration
GAGE – Gage
GHB – General Head
HFB – Horizontal Flow Barrier
LAK – Lake
MNW – Multinode Well
MNW2 – Multinode Well 2
RCH – Recharge
RIV – River
SFR – Stream Flow Routing
STR – Stream-Aquifer Interaction
SUB – Subsidence
WEL – Well
UZF – Unsaturated Zone Flow
We will cover most of these in subsequent lectures