## Slide 1: MODFLOW – Optional Packages Part 2
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Optional Packages
MNW – Multinode Well
MNW2 – Multinode Well 2
RCH – Recharge
RIV – River
SFR – Stream Flow Routing
STR – Stream-Aquifer Interaction
SUB – Subsidence
WEL – Well
UZF – Unsaturated Zone Flow
CHB – Time Variant Specified Head
DRN – Drain
DRT – Drain Return Flow
ETS – Evapotranspiration Segments
EVT – Evapotranspiration
GAGE – Gage
GHB – General Head
HFB – Horizontal Flow Barrier
LAK – Lake

## Slide 3: Stream-Aquifer Systems

## Slide 4: River Package
If head is above river stage, flow is from aquifer -> river
If head is below river stage, flow is from river -> aquifer

## Slide 5: Idealized Representation
Hijk = Head in cell
HRIV = Stage in river
CRIV = Conductance of river bottom sediments
RBOT = Elevation of bottom of sediments
QRIV = Flow between aquifer and river

## Slide 6: Case #1 – Head Above River Stage
QRIV = CRIV * (HRIV - Hijk)
(-Q signifies flow out of cell)

## Slide 7: Case #2 – Head Below River Stage But Above River Bottom
QRIV = CRIV * (HRIV - Hijk)

## Slide 8: Case #3 – Head Below River Bottom
QRIV = CRIV * (HRIV - RBOT)

## Slide 9: River Conductance
Length of reach in each river cell is computed

## Slide 10: River Conductance Calculation
Length of overlap of river on cell

## Slide 11: STR - Stream-Aquifer Interaction Package
Like the River Package, water can flow from aquifer to stream or vice versa.
Unlike the River Package, stage is not specified. Rather, flow is routed using simple channel hydraulics and a stage is computed using Manning’s equation.

## Slide 12: STR Package - Segments and Reaches

## Slide 13: STR Package - Required Attributes
Segments
  Incoming flow (for top segments and diversions)
  Width
  Slope
  Manning’s roughness coefficient
Reaches
  Conductance
  Elevation of the bottom of the streambed
  Elevation of the top of the streambed

## Slide 14: SFR - Stream Flow Routing Package
More advanced stream package
More options for inputs to streams
Interaction with the Unsaturated Zone Flow package

## Slide 15: GHB - General Head Package
Often used to simulate lakes, reservoirs
Required parameters:
  Head
  Conductance

## Slide 16: General Head
Q = Cgh * (Hsource - Hijk)

## Slide 17: General Head Boundary
Gaining Lake/Reservoir
Losing
Lake/Reservoir

## Slide 18: Lakes and Reservoirs

## Slide 19: CHD - Time Variant Specified Head Package
CHD = Changing Head
Original method for defining specified heads, works for static (steady-state) heads only
  IBOUND
  Starting Heads Array
CHD later added to allow for transient specified head boundary conditions
Can be used for steady-state case also

## Slide 20: HFB – Horizontal Flow Barrier Package
Used to simulate low permeability barriers such as faults, sheet pile walls, and slurry trenches

## Slide 21: HFB Cell Boundaries

## Slide 22: HFB – Hydraulic Characteristic
Each instance is assigned a “hydraulic characteristic”
Adjacent Cells
Barrier is applied to the cell boundary
A = Area
T = Thickness

## Slide 23: EVT – Evapotransporation Package
Simulates groundwater loss from evaporation and transpiration
ET rate depends on water table elevation

## Slide 24: EVT – Evapotransporation Package
ET rate = 0.0 when head below (ET surface – ext. depth)
ET rate = Max. ET rate when head above or equal to ET surface
ET rate varies when head between ET surface and ext. depth
User specifies:
Maximum ET rate
Surface elevation (usually ground surface)
Extinction depth