## Slide 1: 2D Geostatistics Interpolating Layer Elevations
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Grid Layer Elevations
Each cell has a top and bottom elevation. The elevation arrays are part of the discretization file used by Groundwater Flow Process.
They are defined/edited in the Global/Basic Package dialog in GMS.
Elevations can be interpolated using 2D geostatistics (interpolation) tools in the 2D Scatter Point Module in GMS.

## Slide 3: Top and Bottom Elevations
Required arrays
  Top elevation for layer 1
  Bottom elevation for all layers
Top1
Top2 = Bot1
Top3 = Bot2
Top4 = Bot3
Bot4
GMS assumes boti = topi+1

## Slide 4: Ground Surface Elevations
For the ground surface elevations (top elevation of layer 1), we can typically download and interpolate digital elevation model (DEM) data.
Steps:
  Select File|Import from Web command
  Locate region
  Select world elevation data
  Interpolate from resulting DEM to MODFLOW layer array

## Slide 5: Map Locator
This appears after selecting the File|Import from Web command. Use it to zoom in on the location where you want to download DEM data.

## Slide 6: Select Data Service

## Slide 7: Interpolate to MODFLOW Layer Array

## Slide 8: Interpolating Other Layer Elevations
Steps:
  Import/Create scatter point sets using data from boreholes, cross sections, etc
  Interpolate to layers
  Fix errors (when necessary)

## Slide 9: Scatter Point Sets
Each set contains
  a list of points with an XY location
  a list of data sets

## Slide 10: Scatter Data Import Options
Prepare tabular scatter point data file
Two import options:
  Save as *.txt or *.cvs and import to GMS using File|Open command
  Copy table in Excel and paste to GMS using Windows Clipboard
Follow Text Import Wizard

## Slide 11: Sample Scatter Point Data

## Slide 12: Import Wizard – Step 1
Be sure to turn this on if there is a header row

## Slide 13: Import Wizard – Step 2
Select type for each column
Select data type here

## Slide 14: Interpolation
You can interpolate from any one of the scatter point data sets to:
  TIN Elevations
  Meshes (2D or 3D)
  Grids (2D or 3D)
  MODFLOW data array layers
A new data set is created on the target object
Notes: 14

## Slide 15: 2D Interpolation Schemes

## Slide 16: Comparing Interpolation Schemes
Elliptical Control Function

## Slide 17: Comparing Interpolation Schemes
Linear

## Slide 18: Comparing Interpolation Schemes
IDW - Constant

## Slide 19: Comparing Interpolation Schemes
IDW – Gradient Planes

## Slide 20: Comparing Interpolation Schemes
IDW – Quadratic, Truncated

## Slide 21: Comparing Interpolation Schemes
Natural Neighbor, Truncated

## Slide 22: Comparing Interpolation Schemes
Kriging

## Slide 23: Summary


Poor
Average
Good

## Slide 24: Interpolating to Layers
Use the Interpolate -> MODFLOW Layers command
Interpolates directly to appropriate layer arrays

## Slide 25: Fixing Errors
Interpolation often causes overlapping elevations
Errors can be detected and fixed using the Model Checker

## Slide 26: Complex Stratigraphy
Interpolation and layer fixing tools can be used to model complex stratigraphic relationships
Bedrock Truncation
Layer Outcropping