## Slide 1: Model Calibration
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Calibration
Solution is computed by model
Simulated heads and flows are compared to field observed values
Input parameters (K, recharge, etc.) are adjusted until model outputs match field observations

## Slide 3: Head Observations

## Slide 4: Flow Observations
Used to analyze gains/losses to baseflow

## Slide 5: Types of Calibration
Trial and error
  Manually tweak inputs and re-run model
Automated parameter estimation
  Optimization utility is used to adjust input parameters in a systematic fashion

## Slide 6: When is a model “calibrated”?
We should not expect a perfect fit between simulated and observed values due to:
  Measurement error
  Simplifying assumptions
  Uncertainty in inputs (river stages, estimated pumping rates, etc.)
We generally try to get the simulated values within a certain “window” of the field observations:
Eventually you reach a point of diminishing returns

## Slide 7: Calibration Error Norms
Mean Error
Mean Absolute Error
Root Mean Squared Error
Each error norm provides a numerical measure of how well the model is calibrated overall

## Slide 8: Error Norms, cont.
where:
Weighted errors:
Standard deviation can be derived from interval and confidence

## Slide 9: Error Norms, cont.
where:
Sum of Squared Weighted Residuals:

## Slide 10: Flow Observations
Represents
  Gain/loss in streams
  Gain/loss in reservoirs and lakes
If flow observations are not included, the solution may be non-unique
+Q
-Q

## Slide 11: Model Uniqueness
Consider a model of a basin where the only input is recharge. Water leaves system through stream and spec. head boundary. Main parameters are recharge and K.
Let’s look at cross section through main axis of site (next slide)

## Slide 12: Model Uniqueness
In order to lower water table:
  Increase K (water leaves system more rapidly)
  Reduce Recharge (less water entering system)
In order to raise water table:
  Decrease K (causes water to mound, raising water table)
  Increase Recharge (causes water to mound)
Calibration is achieved by adjusting parameters so that the water table raises or lowers until it fits the head observations

## Slide 13: Model Uniqueness
Looking at head observations only, calibration can be achieved via:
Low K, low recharge
High K, high recharge
Theoretically, there are an infinite number of combinations of recharge/K that will “calibrate” the model

## Slide 14: Model Uniqueness
If we include a flow observation for the stream, we eliminate one unknown/degree of freedom from the system since the recharge then becomes fixed.
The only remaining unknown is then the hydraulic conductivity (K) and the number of combinations of parameters resulting in “calibration” is drastically reduced  A unique model/solution

## Slide 15: Example
K=0.8
R=0.0012
Error (SSWR) = 142
K=0.2
R=0.0003
Error (SSWR) = 157
In both cases, R is fixed and K is allowed to vary.

## Slide 16: Example, cont.
In this case, we add a flow observation to the river network and solve again for K and R
K=0.42
R=0.00067
Error (SSWR) = 125 (including flow error)