## Slide 1: Parameter Estimation The Pilot Point Method
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Aquifer Heterogeneity
Aquifer properties vary spatially
Sometimes it is difficult to select discreet zones with constant properties
We need a method that simulates heterogeneity with a small number of parameters

## Slide 3: The Pilot Point Method
The properties of the aquifer are spatially interpolated from point data.
The user creates a set of “pilot points” and assigns a parameter value to each (K, Recharge)

## Slide 4: Pilot Points
PEST warps the interpolated surface by adjusting the values at the pilot points based on feedback from observations during the parameter estimation process.

## Slide 5: Pilot Point Advantages
Can produces calibrated models with low error
Does not require arbitrary zonation

## Slide 6: Pilot Point Disadvantages
Longer run times
  1 parameter created for each point
  More parameters require more model runs
Decrease time by using:
  SVD-Assist
  Parallel PEST

## Slide 7: Tikhonov Regularization
PEST uses regularization to:
  add stiffness to the objective function
  allow for more parameters than observations
# Observations: 25
# Parameters: 85
Normally #parameters must be < #observations

## Slide 8: Regularization Options
Preferred homogenous regularization*
  In the absence of any strong influence from the PEST objective function, pilot points that are near to one another should have about the same value.
Preferred value regularization
  In the absence of any strong influence from the PEST objective function, the pilot point values should be equal to their starting value.
Both methods provide stiffness and stability to the solution
*default method

## Slide 9: Creating Pilot Points
Pilot points are 2D Scatter Points
User selects a 2D Scatter Point Set and dataset
Values at points are interpolated to the MODFLOW array

## Slide 10: Creating Pilot Points
Adaptive Placement
  Manually create points in a non-uniform fashion
  Points are strategically located based on obs well and boundary locations
Uniform Placement
  Grid-based distribution
  Simpler and works well in many cases

## Slide 11: Adaptive Placement Strategy
Pilot point
Observation well
Fixed head boundary
Piezometric contour
Points placed between fixed head boundary and nearest downhill observation wells
Points placed between observation wells
Points placed along zone of high hydraulic gradient
Greater point density reflects greater observation well density
Pump-tested well: pilot point and well coincident
Points placed at rear and sides of model domain

## Slide 12: Uniform Placement
Or use the Grid Frame to uniformly distribute a set of points.
Steps
Create a Grid Frame
Select Map -> 2D Grid and enter desired number of rows and columns.
Convert 2D grid to scatter point set.

## Slide 13: Field Data
Pilot points can use field data for measured HK

## Slide 14: Field Data
Select point and use Properties dialog
Turn on the “Fixed Pilot Point” option

## Slide 15: Field Data
The HK array estimated by PEST will not change the measured value