## Slide 1: Boundary Condition Analysis Pt 2 – Selecting Proper Boundary Conditions
CE 547 – BRIGHAM YOUNG UNIVERSITY

## Slide 2: Boundary Condition Analysis
It is critical to select boundary conditions
  That are appropriate for site being studied
  That do not lead to artificial calibration
Common source of model error!

## Slide 3: Example 2
Industrial Plant
River
Mountain Range
What boundary conditions should be used?

## Slide 4: Local Scale
Head Contours
Obs. Wells
Plume

## Slide 5: Simple Approach
Fixed Head BC
No Flow

## Slide 6: Cross-Section View
Bottom Elevation
Left Head BC
Right Head BC
Computed Head
Head Observations

## Slide 7: Darcy’s Law
where:
Q = DVol/Dt = flow rate [L3/T]
K = hydraulic conductivity [L/T]
i = hydraulic gradient [L/L]
A = gross cross-sectional area of flow [L2]
Dh = head loss [L]
L = length of flow path [L]

## Slide 8: Darcy’s Law
H1
H2
L
T
Assumptions:
K = constant T = ave thickness W = width Minimal recharge
Q
K

## Slide 9: Variables
L, T, W  Geometric constants
H1 – H2  Specified by user
Q, K  Independent variables

## Slide 10: Variables, Cont.
Method 1
  Specify K, model solves for Q
Method 2
  Specify Q, model solves for K

## Slide 11: Model Non-Uniqueness
Distribution of heads is not a variable!
Model will produce the same head distribution regardless of what value of K is specified
Left Head BC
Right Head BC
Computed Head
Head Observations

## Slide 12: Avoiding Non-Unique Models
Specified flow boundary conditions
Flow observations
Regional to local model conversion

## Slide 13: Specified Flow Conditions
No Flow BC
Right Head BC
Recharge
Extend upper boundary back to no flow boundary (outcropping or g.w. divide)
Q
Q is now tied to recharge and heads will rise and fall based on K. For a given recharge value, unique K can be found.

## Slide 14: Flow Observations
Stream gages
  Measured gain or loss between two gages in a stream
Tracer tests
  Can be used to estimate Vs, Vd, and Q
Lateral inflow
  Can sometimes be estimated

## Slide 15: Flow Observations, Cont.
Computed flow through right BC is compared to observed flow, Q’
Heads are still fixed by BC, but flow is fixed, and unique K can be found
Observed Flow Q’
Left Head BC
Right Head BC

## Slide 16: Best Case
Observed flow results in unique value of recharge
Fixed Q and observed heads result in unique value of K
No Flow BC
Right Head BC
Recharge
Flow-based upstream BC and a flow observation
Q
Observed Flow Q’

## Slide 17: Regional to Local Conversion
In many cases, flow observations are not available and there are no head or flow boundaries close by
Strategy
  Build regional model corresponding to well-defined boundary conditions
  Use heads/flows from regional model to develop boundary conditions for local model
  K, recharge and other model parameters derived from the regional model

## Slide 18: Regional Model

## Slide 19: Local Grid Boundaries
Head
Head
No-flow
No-flow

## Slide 20: Local Model